## Slide 1: Klub Knoll Workshop
Raspberry Pi Pico

## Slide 2: Agenda
Raspberry Pi
Udviklingsmiljø
UCN RPiP Board
GPIO
Python Libraries
Filer
PWM
A/D konverter
PIO
RP2 board
Links

## Slide 3: Raspberry Pi

## Slide 4: Raspberry Pi Foundation
Grundlaget for udviklingen af RP skal findes helt tilbage i 2006 hvor de faldet færdigheder hos studerende, der søgte ind på Datalogi studiet gav anledning til bekymring blandt en gruppe universitets undervisere, der omfattede Eben Upton Broadcom, Rob Mullins, Jack Lang og Alan Mycroft ved University of Cambridge's Computer Laboratory.
Gruppen af undervisere mente der var et behov for en lille, prisbillig og simpel computer, der kunne anvendes til hobby brug. Flere versioner af de tidlige Raspberry Pi prototyper blev designet, men var meget begrænset af de høje omkostninger og lav ydelse i processorer til mobile enheder på det tidspunkt.
I 2008 startede teamet et samarbejde med Pete Lomas, Norcott Technologies og David Braben, og dannede Raspberry Pi Foundation. Tre år senere blev Raspberry Pi Model B født, og den solgte over to millioner enheder inden for de første to år!!.

## Slide 5: Versioner af RPi
Navn | Model | Hukommelse | Form Factor | Ethernet | Wireless | GPIO | Udgivet
Raspberry Pi | B | 256 MiB | Standard | Ja | Nej | 26-pin | 2012
 | A |  |  | Nej |  |  | 2013
 | B+ | 512 MiB |  | Ja |  | 40-pin | 2014
 | A+ |  | Compact | Nej |  |  | 2014
Raspberry Pi 2 | B | 1 GiB | Standard | Ja | Nej |  | 2015
Raspberry Pi Zero | Zero | 512 MiB | Zero | Nej | Nej |  | 2015
 | W/WH |  |  |  | Ja |  | 2017
Raspberry Pi 3 | B | 1 GiB | Standard | Ja | Ja ( 2.4 GHz) |  | 2016
 | A+ |  | Compact | Nej |  |  | 2018
 | B+ |  | Standard | Ja |  |  | 2018
Raspberry Pi 4 | B | 1 GiB | Standard | Ja | Ja (også 5 GHz) |  | 2019
 |  | 2 GiB |  |  |  |  | 
 |  | 4 GiB |  |  |  |  | 
 |  | 8 GiB |  |  |  |  | 2020
 | 400 (4 GiB) | 4 GiB | Keyboard |  |  |  | 
Raspberry Pi Pico | N/A | 264 KiB | Pico (21 mm × 51 mm) | Nej | Nej | 26-pin | 2021

## Slide 6: Versioner af Raspberry PI CM
1.5GHz quad-core 64-bit ARM Cortex-A72 CPU
VideoCore VI graphics, supporting OpenGL ES 3.x
4Kp60 hardware decode of H.265 (HEVC) video
1080p60 hardware decode, and 1080p30 hardware encode of H.264 (AVC) video
Dual HDMI interfaces, at resolutions up to 4K
Single-lane PCI Express 2.0 interface
Dual MIPI DSI display, and dual MIPI CSI-2 camera interfaces
1GB, 2GB, 4GB or 8GB LPDDR4-3200 SDRAM
Optional 8GB, 16GB or 32GB eMMC Flash storage
Optional 2.4GHz and 5GHz IEEE 802.11b/g/n/ac wireless LAN and Bluetooth 5.0
Gigabit Ethernet PHY with IEEE 1588 support
28 GPIO pins, with up to 6 × UART, 6 × I2C and 5 × SPI

## Slide 7: Raspberry Pi Pico
Is a low-cost, high-performance microcontroller board with flexible digital interfaces.
Key features include:
RP2040 microcontroller chip designed by Raspberry Pi in the United Kingdom
Dual-core Arm Cortex M0+ processor, flexible clock running up to 133 MHz
264KB of SRAM, and 2MB of on-board Flash memory
Castellated module allows soldering direct to carrier boards
USB 1.1 with device and host support
Low-power sleep and dormant modes
Drag-and-drop programming using mass storage over USB
26 × multi-function GPIO pins
2 × SPI, 2 × I2C, 2 × UART, 3 × 12-bit ADC, 16 × controllable PWM channels
Accurate clock and timer on-chip
Temperature sensor
Accelerated floating-point libraries on-chip
8 × Programmable I/O (PIO) state machines for custom peripheral support
https://sketchfab.com/3d-models/raspberry-pi-pico-79aba8c863a14b4682e34e241f2159d2

## Slide 8: Hvad er specielt ved RPiP
Ingen operativsystem !!, men filsystem uf2 (microsoft) og boatloader (bootselect)
Meget lavt strømforbrug (for en typisk applikation en faktor 100 i forhold til RPi4)
Billig RPiP 24dkr (hvis den kan fås !), processor RP2040 sælges løst.
Meget fleksibel I/O, relokerbare i/o-funktioner, programmerbar I/O (PIO)
Flere muligheder for low power via dynamisk klokfrekvens, sleep og dorment mode.
Udviklingsmiljøer: C/C++, MicroPython, CircuitPython (Adafruit), Arduino kommer og (Java ME måske??!)

## Slide 9: Udviklingsmiljø

## Slide 10: MicroPython
MicroPython is a lean and efficient implementation of the Python 3 programming language that includes a small subset of the Python standard library and is optimised to run on microcontrollers and in constrained environments.
The MicroPython runs on the bare metal, giving you a low-level Python “operating system” that can be used to control all kinds of electronic projects.
Kilde: https://micropython.org/

## Slide 11: Installation af MicroPython
Forbind Board via USB til din PC, der skulle gerne vise sig et nyt drev i File Explorer med navnet ”RPI-RP2”.
Filen rp2-pico-20210324-unstable-v1.14-121-g4fc2866f4.uf2 I skulle have downloaded fra https://micropython.org/download/rp2-pico/ trækkes nu over på RPI-RP2 drevet.
Board genstarter og er nu klar til at modtage pythonkode via com port (nr kan ses i ”Device manager”)

## Slide 12: Thonny
Menu
ToolBar
Editor
REPL (”Shell”)
Target selector

## Slide 13: Target
Thonny kan forbinde til forskellige target vælg ”MicroPython (Raspberry Pi Pico”) herefter vil REPL sende input til RPiP og modtage output fra RPiP.

## Slide 14: Hello World
For at udskrive i python bruges funktionen print(”bla bla”)
Lav et program der udskriver en lille tekst
  Indtast program i Editor vinduet
  Gem program på Raspberry Pi Pico
  Kør program ved at trykke
  Er output som forventet ?
  Hint programmet kan gøres lidt mere spændende ved at indlæst input fra bruger:
  navn = input(”Hvad er dit navn?”)

## Slide 15: UCN Board

## Slide 16: UCN Board
Raspberry Pi Pico

## Slide 17: UCN Board
Raspberry Pi Pico
ESD protected input (output)

## Slide 18: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger

## Slide 19: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer

## Slide 20: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer
Rest bottom

## Slide 21: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer
Reset Bottom
SD-Card Connector

## Slide 22: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer
Reset Bottom
SD-Card Connector
User bottom

## Slide 23: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer
Reset Bottom
SD-Card Connector
3 User bottom
3 Led

## Slide 24: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer
Reset Bottom
SD-Card Connector
3 User bottom
3 Led
Pin header directly connected to RPiP

## Slide 26: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer
Reset Bottom
SD-Card Connector
3 User bottom
3 Led
Pin header directly connected to RPiP
Jumper for connecting ESD protected input, buzzer and SD-Card Connector

## Slide 27: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer
Reset Bottom
SD-Card Connector
3 User bottom
3 Led
Pin header directly connected to RPiP
Jumper for connecting ESD protected input, buzzer and SD-Card Connector
RP2040 Processor

## Slide 28: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer
Reset Bottom
SD-Card Connector
3 User bottom
3 Led
Pin header directly connected to RPiP
Jumper for connecting ESD protected input, buzzer and SD-Card Connector
RP2040 Processor
Micro USB socket

## Slide 29: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer
Reset Bottom
SD-Card Connector
3 User bottom
3 Led
Pin header directly connected to RPiP
Jumper for connecting ESD protected input, buzzer and SD-Card Connector
RP2040 Processor
Micro USB socket
Bootselect

## Slide 30: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer
Reset Bottom
SD-Card Connector
3 User bottom
3 Led
Pin header directly connected to RPiP
Jumper for connecting ESD protected input, buzzer and SD-Card Connector
RP2040 Processor
Micro USB socket
Bootselect
Debug interface

## Slide 31: UCN Board
Raspberry Pi Pico
ESD protected input (output)
LiPo batterie connector and charger
Buzzer
Reset Bottom
SD-Card Connector
3 User bottom
3 Led
Pin header directly connected to RPiP
Jumper for connecting ESD protected input, buzzer and SD-Card Connector
RP2040 Processor
Micro USB socket
Bootselect bottom
Debug interface
16Mbit Quad SPI flash, 133MHz

## Slide 32: Port Assignment
Item | Port on RPiP | Jumper
led1 | GPIO10 | -
led2 | GPIO11 | -
led3 | GPIO12 | -
sw1 | GPIO13 | -
sw2 | GPIO14 | -
sw3 | GPIO15 | -
Reset | RUN | -
Buzzer | GPIO9 | JP1
Analog#0 | GPIO26/ADC0 | JP5
Analog#1 | GPIO27/ADC1 | JP6
Analog#2 | GPIO28/ADC3 | JP7
SD-DAT0 | GPIO19 | -
SD-DAT1 | GPIO20 | JP3
SD-DAT2 | GPIO21 | JP2
SD-DAT3/CD | GPIO22 | -
SD-CMD | GPIO18 | -
SD-CLK | GPIO5 | JP4

## Slide 33: GPIO
General Purpose I/O

## Slide 34: Nyttig funktion
Har man brug for online hjælp til en Python funktion, konstant eller klasse kan man i REPL benytte kommandoen help().
Eksempel:
Prøv at skrive help() !

## Slide 35: Styring af GPIO med Python
For at tilgå porte skal bibioteket machine først importeres dette:
import machine
Herefter kan porte opsættes til ud eller indgange
led1 = machine.Pin(10,machine.Pin.OUT)
I linien ovenfor er GPIO 10 defineret som output og led1 anvendes når output af port skal sættes.
led1.on()
Kan også skrives som led1.value(1)

## Slide 36: Styring af GPIO med Python
Skal en port være en indgang gøres kan dette gøres ved:
sw1 = machine.Pin(13,machine.Pin.IN)
Værdi af port sw1 kan indlæses ved følgende kode:
if sw1.value()==False:
print(”Port var lav”)
else:
print(”Port høj”)

## Slide 37: Opgave (laves i teams af tre)
Lav et Python program der tænder led1 når sw1 holdes nedtrykket, tænder led2 når sw2 er nedtrykket osv.
Hint en uendelig løkke laves som vist nedenfor:
while True:
bla (det indrykkede er i while blok)
(extra) Modificer program så led blinker når switch holdes nedtrykket Hint:
import time
time.sleep(1.5)
Giver et delay på 1.5 sek

## Slide 38: Python libraries
Der findes en rigtig god dokumentation på micropython.org:
https://docs.micropython.org/en/latest/

## Slide 39: Python standard libraries and micro-libraries
Name | Functionality
_thread | Low-level threading API
array | arrays of numeric data
builtins | builtin functions, constants, exceptions, and decorators
cmath | mathematical functions for complex numbers (ikke implementeret)
gc | control the garbage collector
math | mathematical functions
sys | system specific functions
ubinascii | binary/ASCII conversions
ucollections | collection and container types
uerrno | system error codes (ikke implementeret)

## Slide 40: Python standard libraries and micro-libraries
Name | Functionality
uhashlib | hashing algorithm
uheapq | heap queue algorithm (ikke implementeret)
uio | input/output streams
ujson | JSON encoding and decoding
uos | basic “operating system” services
urandom | Random Number Generation
ure | regular expressions
ustruct | pack and unpack primitive data types
utime | time related functions

## Slide 41: MicroPython-specific libraries
Name | Functionality
rp2 | Raspberry Pi Pico specific
onewire | Driver for onewire devices (ikke implementeret)
neopixel | Driver for neopixel (ikke implementeret)
dht | Driver for DHT devices (ikke implementert)

## Slide 42: MicroPython er under udvikling
Projekt kan følges her:
https://github.com/micropython/micropython

## Slide 43: Opgave (teams af tre)
Lav et program der laver et tilfældeligt tal mellem 1 og 1000, herefter skal man gætte tallet.
Spiller indtaster gæt, er gæt for lavt tændes led 1 er gæt for høj tændes led 3 er gæt korrekt tændes led 2.
Ved næste gæt slukkes led markering for sidste gæt og ovenstående procedure gentages.
Hint anvende urandom.randrange(1000) til at lave tilfældigt tal med

## Slide 44: PWM
Pulse-width modulation

## Slide 45: Pulse-width modulation

## Slide 46: machine.PWM
from machine import Pin, PWM
import time
buzzer = PWM(Pin(9))
while True:
buzzer.freq(440)
buzzer.duty_u16(1000)

## Slide 47: Opgave (team af tre)
Lav et Python program der afspiller en tone når der trykkes på sw1 en anden tone når der trykkes på sw2 osv
(extra) Lav programmet således at lyd niveauet langsomt bliver forøget når switch holdes nedtrykket.

## Slide 48: Filer i MicroPython

## Slide 49: Filer i MicroPython
Der er på RP2 implementer filsystem og fra microPython kan dette anvendes.
Åben fil for skrivning:
myfile = open("temps.txt","w")
Åbenfil for læsning:
myfile = open("temps.txt","w")
Skriv til fil : myfile.write(whateverdata)
Læs fra fil : x=myfile.read()

## Slide 50: Filer i MicroPython
Der findes i biblioteket os en del funktioner til at håndtere filsystemet:
Navn | Funktion | Navn | Funktion
uname |  | rename | Rename a file
chdir | Change current directory | rmdir | Remove a directory
getcwd | Get the current directory | stat | Get the status of a file or directory
listdir | List the current directory | statvfs | Get the status of a fileystem
mkdir | Create a new directory | ilistdir | This function returns an iterator which then yields tuples corresponding to the entries in the directory that it is listing
remove | Remove a file | mount | Mount the filesystem object fsobj at the location in the VFS given by the mount_point string
 |  | umount | Unmount a filesystem.

## Slide 51: Opgave (Teams af tre)
Lav et Python program der opretter en fil i direktoriet test og skriver følgende ind i filen:
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
I Thonny kan mulighed for at se filer på RP2 enables under view->files, ligger fil det korrekte sted og har det korrekte indhold ?
Omskriv program så det sletter fil og direktorie

## Slide 52: A/D konverter

## Slide 53: A/D-Konverter
Der er på RP2040 fem A/D-C kanaler. De har en opløsning på 12 bit, 4096 step.
Den femte kanal er dog fast forbundet til en intern temperatur sensor og kan altså ikke anvendes til andet.
Er det ikke nødvendigt med en opløsning på 12 bit kan A/D-C’s opløsning ændres (fra 9 bit til 12bit) dog ikke implementeret i micropython for RP2 
Reference spænding for A/D-C er default sat til 3.3V.

## Slide 54: Brug af A/D-C
Dette lib er ikke helt implementeret og indeholder således kun nedenstående funktion:
object <class 'ADC'> is of type type
read_u16 -- <function>
CORE_TEMP – 4
!! Klassen hedder ADC altså med store bogstaver.
from machine import ADC
adc1=ADC(Pin(1))
value = adc1.read_u16()

## Slide 55
Source: From RP2040 datasheet

## Slide 56: PIO
Programmable input/output block

## Slide 57: PIO

## Slide 58: PIO
Each state machine is equipped with:
Two 32-bit shift registers – either direction, any shift count
Two 32-bit scratch registers
4×32-bit bus FIFO in each direction (TX/RX), reconfigurable as 8×32 in a single direction
Fractional clock divider (16 integer, 8 fractional bits)
Flexible GPIO mapping
DMA interface, sustained throughput up to 1 word per clock from system DMA
IRQ flag set/clear/status

## Slide 59: Instruktions sæt

## Slide 60: PIO eksempel (Blink med led 1Hz)
import time
from machine import Pin
import rp2
@rp2.asm_pio(set_init=rp2.PIO.OUT_LOW)
def blink_1hz():
# Cycles: 1 + 1 + 6 + 32 * (30 + 1) = 1000
irq(rel(0))
set(pins, 1)
set(x, 31) [5]
label("delay_high")
nop() [29]
jmp(x_dec, "delay_high")
# Cycles: 1 + 7 + 32 * (30 + 1) = 1000
set(pins, 0)
set(x, 31) [6]
label("delay_low")
nop() [29]
jmp(x_dec, "delay_low")

## Slide 61: PIO eksempel (Blink med led 1Hz)
# Create the StateMachine with the blink_1hz program, outputting on Pin(25).
sm = rp2.StateMachine(0, blink_1hz, freq=2000, set_base=Pin(25))
# Set the IRQ handler to print the millisecond timestamp.
sm.irq(lambda p: print(time.ticks_ms()))
# Start the StateMachine.
sm.active(1)

## Slide 62: Nye board der anvender RP2040

## Slide 63: Adafruit Feather RP2040

## Slide 64: ItsyBitsy 2040

## Slide 65: Arduino

## Slide 66: Tiny 2040

## Slide 67: Pro Micro - RP2040

## Slide 68: Links

## Slide 69: Relevant Links
https://docs.micropython.org/en/latest/
https://www.raspberrypi.org/products/raspberry-pi-pico/specifications/
https://www.raspberrypi.org/forums/index.php

## Slide 70: Book